## Slide 1: EECE 350 Computer Networks
Spring 2015

## Slide 2: Transport services and protocols
provide logical communication between app processes running on different hosts
transport protocols run in end systems
more than one transport protocol available to apps
  Internet: TCP and UDP
application
transport
network
data link
physical
logical end-end transport
application
transport
network
data link
physical

## Slide 3: Transport vs. network layer
network layer: logical communication between hosts
transport layer: logical communication between processes
  relies on, and can enhance, network layer services

## Slide 4: Internet transport-layer protocols
reliable, in-order delivery (TCP)
  congestion control
  flow control
  connection setup
unreliable, unordered delivery: UDP
  no-frills extension of “best-effort” IP
services not available:
  delay guarantees
  bandwidth guarantees
application
transport
network
data link
physical
application
transport
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
logical end-end transport

## Slide 5: Multiplexing/demultiplexing
process
socket
use header info to deliver
received messages to correct
socket
demultiplexing at receiver:
handle data from multiple
sockets, add transport header (later used for demultiplexing)
multiplexing at sender:
transport
application
physical
link
network
P2
P1
transport
application
physical
link
network
P4
transport
application
physical
link
network
P3

## Slide 6: How de/multiplexing works
host receives IP datagrams
  each datagram has source IP address, destination IP address
  datagram may carry a transport-layer “segment”
  each segment has source, destination port number
host uses IP addresses & port numbers to direct segment to appropriate socket
source port #
dest port #
32 bits
application
data
(payload)
other header fields
segment format

## Slide 7: UDP: User Datagram Protocol [RFC 768]
“no frills,” “bare bones” Internet transport protocol
“best effort” service, UDP messages may be:
  lost
  delivered out-of-order to app
connectionless:
  no handshaking between UDP sender, receiver
  each UDP message handled independently of others
UDP use:
  streaming multimedia apps (loss tolerant, rate sensitive)
  DNS (domain name)
  SNMP (network management)
reliable transfer over UDP:
  add reliability at application layer
  application-specific error recovery!

## Slide 8: UDP header
source port #
dest port #
32 bits
application
data
(payload)
UDP message format
length
checksum
length, in bytes of UDP message, including header
no connection establishment (which can add delay)
simple: no connection state at sender, receiver
small header size
no congestion control: UDP can blast away as fast as desired
why is there a UDP?

## Slide 9: UDP Header
source port (16 bits) - could be zero if not used
destination port (16 bits)
UDP message length (16 bits) - header and data
UDP checksum (16 bits)
  optional for low overhead
  check that data arrives correctly
  uses a pseudo-header in computation

## Slide 10: UDP Pseudo-Header
Verifies that UDP datagram reaches its correct destination
  specific machine and specific protocol port
UDP on the sending machine computes a checksum that covers the IP addresses and the UDP datagram
Since the IP is a layer “below” this, we must copy the IP addresses into a pseudo-header

## Slide 11: UDP Pseudo-Header

## Slide 12: Example Checksum Calculation
    UDP datagram going from IP address 153.18.8.105, port 1087 to IP address 171.2.14.10, port 13. The UDP message is “TESTING”

## Slide 13: Encapsulation and Decapsulation two hosts on the same subnet

## Slide 14: UDP Port Numbers
Computers need to agree on port numbers and their meaning
Well-known ports are permanently assigned for specific applications
Dynamic binding
  assigned by the network software when a program needs a port

## Slide 15: Well-Known UDP Port Numbers
Port Number | Service
7 | Echo
9 | Discard
13 | Daytime
37 | Time
53 | Domain
69 | TFTP
161 | SNMP
514 | Syslog
520 | Routed (RIP)

## Slide 16: NAT: network address translation
10.0.0.1
10.0.0.2
10.0.0.3
10.0.0.4
138.76.29.7
local network
(e.g., home network)
10.0.0/24
rest of
Internet
datagrams with source or
destination in this network
have 10.0.0/24 address for
source, destination (as usual)
all datagrams leaving local
network have same single source NAT IP address: 138.76.29.7,different source port numbers

## Slide 17: NAT: network address translation
motivation: local network uses just one IP address as far as outside world is concerned:
  range of addresses not needed from ISP: just one IP address for all devices
  can change addresses of devices in local network without notifying outside world
  can change ISP without changing addresses of devices in local network
  devices inside local net not explicitly addressable, visible by outside world (a security plus)

## Slide 18: NAT: network address translation
implementation: NAT “router” must:
  outgoing datagrams: replace (source IP address, port #) of every outgoing datagram to (NAT IP address, new port #)
    . . . remote clients/servers will respond using (NAT IP address, new port #) as destination address
  remember (in NAT translation table) every (source IP address, port #) to (NAT IP address, new port #) translation pair
  incoming datagrams: replace (NAT IP address, new port #) in destination fields of every incoming datagram with corresponding (source IP address, port #) stored in NAT table

## Slide 19: NAT: network address translation
10.0.0.1
10.0.0.2
10.0.0.3
S: 10.0.0.1, 3345
D: 128.119.40.186, 80
1
10.0.0.4
138.76.29.7
1: host 10.0.0.1
sends datagram to
128.119.40.186, 80
NAT translation table
WAN side addr LAN side addr
138.76.29.7, 5001 10.0.0.1, 3345
…… ……
S: 128.119.40.186, 80
D: 10.0.0.1, 3345
4
S: 138.76.29.7, 5001
D: 128.119.40.186, 80
2
2: NAT router
changes datagram
source addr from
10.0.0.1, 3345 to
138.76.29.7, 5001,
updates table
S: 128.119.40.186, 80
D: 138.76.29.7, 5001
3
3: reply arrives
dest. address:
138.76.29.7, 5001
4: NAT router
changes datagram
dest addr from
138.76.29.7, 5001 to 10.0.0.1, 3345

## Slide 20: DNS: domain name system
people: many identifiers:
  ID number, name, passport #
Internet hosts, routers:
  IP address (32 bit or 128 bit)
  “name”, e.g., www.yahoo.com - used by humans
Q: how to map between IP address and name, and vice versa ?
Domain Name System:
distributed database implemented in hierarchy of many name servers
application-layer protocol: hosts, name servers communicate to resolve names (address/name translation)
  note: core Internet function, implemented as application-layer protocol
  complexity at network’s “edge”

## Slide 21: DNS: services, structure
why not centralize DNS?
single point of failure
traffic volume
distant centralized database
maintenance
DNS services
hostname to IP address translation
host aliasing
  canonical, alias names
mail server aliasing
load distribution
  replicated Web servers: many IP addresses correspond to one name
A: doesn’t scale!

## Slide 22: DNS: a distributed, hierarchical database
Root DNS Servers
com DNS servers
org DNS servers
edu DNS servers
aub.edu
DNS servers
mit.edu
DNS servers
yahoo.com
DNS servers
amazon.com
DNS servers
ieee.org
DNS servers
client wants IP for www.amazon.com; 1st approx:
client queries root server to find com DNS server
client queries com DNS server to get amazon.com DNS server
client queries amazon.com DNS server to get IP address for www.amazon.com
…
…

## Slide 23: DNS: root name servers
contacted by local name server that can not resolve name
root name server:
  contacts authoritative name server if name mapping not known
  gets mapping
  returns mapping to local name server
13 root name “servers” worldwide
a. Verisign, Los Angeles CA
(5 other sites)
b. USC-ISI Marina del Rey, CA
l. ICANN Los Angeles, CA
(41 other sites)
e. NASA Mt View, CA
f. Internet Software C.
Palo Alto, CA (and 48 other sites)
i. Netnod, Stockholm (37 other sites)
k. RIPE London (17 other sites)
m. WIDE Tokyo
(5 other sites)
c. Cogent, Herndon, VA (5 other sites)
d. U Maryland College Park, MD
h. ARL Aberdeen, MD
j. Verisign, Dulles VA (69 other sites )
g. US DoD Columbus, OH (5 other sites)

## Slide 24: TLD, authoritative servers
top-level domain (TLD) servers:
  responsible for com, org, net, edu, …, and all top-level country domains, e.g.: uk, fr, ca, jp, lb
authoritative DNS servers:
  organization’s own DNS server(s), providing authoritative hostname to IP mappings for organization’s named hosts
  can be maintained by organization or service provider

## Slide 25: Local DNS name server
does not strictly belong to hierarchy
each ISP (residential ISP, company, university) has one
  also called “default name server”
when host makes DNS query, query is sent to its local DNS server
  has local cache of recent name-to-address translation pairs (but may be out of date!)
  acts as proxy, forwards query into hierarchy

## Slide 26: DNS name resolution example
requesting host
cis.poly.edu
gaia.cs.umass.edu
root DNS server
local DNS server
dns.poly.edu
1
2
3
4
5
6
authoritative DNS server
dns.cs.umass.edu
7
8
TLD DNS server
host at cis.poly.edu wants IP address for gaia.cs.umass.edu
iterated query:
contacted server replies with name of server to contact
“I don’t know this name, but ask this server”

## Slide 27
4
5
6
3
recursive query:
puts burden of name resolution on contacted name server
heavy load at upper levels of hierarchy?
requesting host
cis.poly.edu
gaia.cs.umass.edu
root DNS server
local DNS server
dns.poly.edu
1
2
7
authoritative DNS server
dns.cs.umass.edu
8
DNS name resolution example
TLD DNS
server

## Slide 28: DNS: caching, updating records
once (any) name server learns mapping, it caches mapping
  cache entries timeout (disappear) after some time
  TLD servers typically cached in local name servers
    thus root name servers not often visited
cached entries may be out-of-date
  if host changes IP address, may not be known Internet-wide until all cached entries expire